## Slide 1: RASSA: Resistive Pre-Alignment Accelerator for Approximate DNA Long Read Mapping
Department of Electrical Engineering
Technion
Roman Kaplan, Leonid Yavits and Ran Ginosar
Silver medal winner in SC18 ACM Student Research Competition
Published in IEEE Micro, Jan-Feb 2019 issue

## Slide 2: Motivation: Faster Genome Assembly
Many options exist once the genomic code is known:
  Precision medicine: e.g., improved cancer treatment
  Genetic risk factors detection
  On-site disease detection
Assembling the genome is computationally difficult
 Takes hours on a high-end machine
Sequencing
DNA Reads
DNA
molecule
Sequencing machine
No Reference
Reference
Exists
30-50x

## Slide 3: Why Bioinformatics Requires Acceleration?
Reduced costs  Exponentially growing database sizes
Large samples: human genome=3Gbp. Sequencing requires ~30×
Even worse in other fields, like Metagenomics
Source: https://www.ncbi.nlm.nih.gov/genbank/statistics/
1Tbp
10Tbp
100Gbp
10Gbp
GenBank
Moore’s Law
Whole-Genome Sequencing

## Slide 4: Problem: Long DNA Read Mapping
Major step in constructing a genome, when a reference sequence exists (e.g., human)
Informal Definition: Find the location of every sequenced read on the reference sequence
AGCTTAGCTCGCATAGCTCCCGAAATCGCTAAATGCGCCCTAGGCTAGCT
TAGCTCCCGAAATCGCTGAAT
Reference Sequence
GCACCAGACTAGCT
GGGTTAACTCG
…
…
…
…
“Easier” with 1st (1970+) and 2nd (2000+) generation sequenced reads:
Low error rate (<1%)
Fixed-length, short reads: 100-600bp in length
2nd generation sequencing exists since the ~2000s  Many tools, heuristics and methods exist for short read mapping
Sequenced Reads
Mapping
AGCTCGCATAGCTCCCGAAA
AATGCGCCCTAGGCTAGCT

## Slide 5: Problem: 3rd Generation of Sequencing Technologies
Reads are of varying long lengths: 1kbp-60kbp+
High error rates: ~15% for PacBio, ~20% for ONT
3rd generation continuous to develop
Error rates are reduced
New devices introduced
Constant search of mapping heuristics & high performance is difficult
PacBio Read Lengths Histogram
Challenges of 3rd generation sequencing (since 2010)
Sources: [right] Rhoads, Anthony, and Kin Fai Au. "PacBio sequencing and its applications." Genomics, proteomics & bioinformatics 13.5 (2015): 278-289.
[left] https://nanoporetech.com
Existing read mapping tools do not work well when changing read characteristics

## Slide 6: Our Approach For Mapping Long Reads
Reference Sequence
(Stored on memory)
C A C T T C A C C T A A G T G A G C A T G A A T G T T C A C G T G T C T G C T G G C A T A C A G A G
Read chunk
C C T A G T G A G C A T G A A C G T T C A C A G T G T C T G
Chart: Mismatch Score vs. Cycle Number
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Mismatch Score | 0.76667 | 0.7 | 0.66667 | 0.86667 | 0.76667 | 0.76667 | 0.8 | 0.56667 | 0.36667 | 0.83333 | 0.8 | 0.8 | 0.73333 | 0.9 | 0.63333 | 0.73333 | 0.76667 | 0.83333 | 0.66667 | 0.9 | 0.66667 | 0.86667 | 0.76667 | 0.86667 | 0.6
Threshold (50% mismatches) | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
1. Split the long reads to short fixed-length chunks
2. Use Hamming Distance with Sliding Window Search
 Find location with high match score = low mismatch score

## Slide 7: So What’s New? Memristors
Change resistance with applied voltage
Non volatile
Zero leakage
High endurance ()
CMOS-compatible
Can be placed in metal layers above silicon
Small area footprint: 4F2
High
Resistance
Low
Resistance

## Slide 8: Architecture: The Basic 1Bit Cell
Basic 1bit cell: 2 transistors, 1 memristor (2T1R)
Storing Values
Stored ‘0’: Memristor in low resistive state ()
Stored ‘1’: Memristor in high resistive state ()
Compare to ‘1’: Mismatch
Compare to ‘0’: Match
Example: Stored ‘0’
No charge flow
 No change in Match line voltage
Match line
Selector OFF
Match line
Selector ON
Charge flow
 Match line voltage drop
Evaluation
Discharge before
evaluation starts
Stored value
Compared pattern
(sequenced read)
Parasitic capacitance

## Slide 9: Architecture: Encoding DNA Bases and Counting Mismatches
One-hot encoding: 4 DNA bases  4 bit cells per base
Match Line Voltage Level
15 DNA bases (60 bit cells) share a Match Line
Match
Line
0 mismatches
15 mismatches

## Slide 10: Architecture: Full Chip Design
Match Line voltage is decoded to a digital value: Analog-to-Digital converter
Lower Match Line voltage = mismatch (Match Line counts mismatches)
 Digital values in 4bit: from 0 to 15 mismatches (15 base pairs)
Sub-Word
15 bases × 4 bitcells
= 60 bitcells
Word Row
16 SubWords
(total 240 bases)
Full Chip
Word Rows
31.5 Mbp
Sum
mismatches
Compare to
threshold
Word Row 131K

## Slide 11: How it Works?
Reads are divided to fixed-size chunks: e.g., 200bp
A threshold is set to 40-50% of chunk’s length (determined empirically)
RASSA stores the reference sequence
Every chunk is compared against the entire reference
Map iteration: Compare chunk  Sum mismatches  ≤threshold ?
Chunk Compared with the
Reference Sequence
The Comparison in RASSA
240bp
(Word Row)
240bp
(Word Row)
Word Row 1
Word Row 2
Word Row 3
Chunk 1
Chunk 1
Chunk 1
Chunk 1
Reference Sequence
…
…
Compare chunk 1
Compare chunk 1
Compare chunk 1
200bp
Example comparison, cycle 1
+
+
+
≤
≤
≤
Compared long read
Chunk 1
200 bps
…
200 bps
Chunk 2
Word Row 131K

## Slide 12: How it Works?
Full map iteration: shift chunk right  Compare  Sum  ≤threshold ?
Case: 2 Word Rows are needed to compare a chunk  2 cycles are needed per chunk
1st cycle: compare 1st part of chunk  sum all mismatches (no comparison to threshold)
2nd cycle: compare 2nd part of chunk  sum all misses + misses from 1st cycle  ≤threshold ?
Example: 2 cycles for mismatch count
Chunk Compared with Ref Seq
Ref seq
RASSA: Cycle 140
…
Comp chunk 1
Comp chunk 1
Comp chunk 1
+
+
+
≤
≤
≤
RASSA: Cycle 141
200bp
Word Row 1
Word Row 2
Word Row 3
Chunk 1
1
Current cycle
Next cycle
Word Row 4
Word Row 131K

## Slide 13: How it Works?
Full map iteration: shift chunk right  Compare  Sum  ≤threshold ?
Case: 2 Word Rows are needed to compare a chunk  2 cycles are needed per chunk
1st cycle: compare 1st part of chunk  sum all mismatches (no comparison to threshold)
2nd cycle: compare 2nd part of chunk  sum all misses + misses from 1st cycle  ≤threshold ?
Example comparison, cycles 140-141
Chunk Compared with Ref Seq
…
≤
≤
≤
Ch. 1
Ch. 1
Ch. 1
+
+
+
RASSA: Cycle 141
Ref seq
W R 2
W R 3
W R 4
Inactive
Active
Chunk
1
Word Row 131K

## Slide 14: Full Chip Parameters
Sub-Word circuit designed, placed and routed using 28nm Global Foundries CMOS High-K Metal Gate library for:
  Transistor sizing
  Timing
  Power analysis
Spectre simulations for FF and SS corners at 700c and nominal voltage
Parameter | Value
DNA bps per row (bits) | (960)
Words per chip | ()
Memory size (DNA bps) | 
Node Technology | 28nm
Frequency | 1
Max chip power | (usually 50% active)
Chip area | 
Parameter | Value
DNA bps per row (bits) | 
Words per chip | 
Memory size (DNA bps) | 
Node Technology | 28nm
Frequency | 
Max chip power | 
Chip area | 

## Slide 15: Evaluation 1: Comparison with Read Mapping Tool
Comparison with state-of-art read mapping tool: minimap2 [1]
  Uses multi-threading & SIMD extensions
Executed system: Intel Xeon E5-2650 @2GHz w/ 16-cores, 64GB of RAM
Results
  Sensitivity: % of reads where RASSA matches minimap2
  False positives: % of incorrect mappings by RASSA
[1] Li, Heng. "Minimap2: pairwise alignment for nucleotide sequences." Bioinformatics 1 (2018): 7.
Reference Seqs
E.coli: 4.6Mbp
Yeast: 12Mbp

## Slide 16: Evaluation 2: Comparison with FPGA
[1] Alser, M., Hassan, H., Xin, H., Ergin, O., Mutlu, O. and Alkan, C. “GateKeeper: a new hardware architecture for accelerating pre-alignment in DNA short read mapping.” Bioinformatics, vol. 33, no. 21, pp. 3355-3363, 2017.
Read/Chunk Lengths | GateKeeper | RASSA @250MHz
100bp | 1.7 BEML/s | 231 BEML/s
200bp | - | 179 BEML/s
300bp | 0.2 BEML/s | 146 BEML/s
RASSA vs. GateKeeper Throughput Comparison
Gatekeeper [1], a pre-alignment FPGA accelerator
  Counts number of mismatches between short reads and a reference sequence
  Implemented in a Virtex-7 FPGA using Xilinx VC709 board, running @250MHz
  Host machine uses 3.6GHz Intel i7-3820 CPU w/ 8GB of RAM
Comparison of RASSA vs. GateKeeper throughput
  Throughput measured in Billion Evaluated Mapping Locations per sec (BEML/s)
  GateKeeper results were taken from [1], RASSA results are normalized to 250MHz

## Slide 17: Conclusions
Increasing database sizes & slowdown in Moore’s law require new approaches: RASSA is a massively-parallel in-memory accelerator
Emerging technologies may provide the next 100× performance-power improvement
  Enable new architectures: memory & processing are combined
 As with Deep Learning, the answer might be specialization (accelerators)
  Bioinformatics acceleration gains more interest in academia
New challenges emerge: programming, designing, testing, etc.

## Slide 18: Thank you