## Slide 1: IMPACT: Interval-based Multipass Proteomic Alignment with Constant Traceback
Sahand Kashani, Stuart Byma, James Larus
2019/02/16
Notes: Recent algorithmic work

## Slide 2: Phylogenetics – The study of evolutionary history between species
Image credit: http://www.oceanographerschoice.com/2009/06/wicked-cool-phylogenetic-tree/

## Slide 3: Evolutionary biology through protein analysis
DNA
Nucleotide chains
  A, C, G, T
Proteins
Amino-acid chains
  A, C, D, E, F, G, H, I, K, L, M, N, P, Q, R, S, T, V, W, Y
Find relationships between species’ proteins
  Cluster “similar” proteins together
  Similarity determined through sequence alignment

## Slide 4: Alignment runtime extremes
Smith-Waterman
  in sequence length
Wide variance in protein lengths
Need an algorithm that
  Works well on short and long proteins
  Can be accelerated in hardware
4 orders of magnitude
Notes: Not the same fixed-length reads that you get out of your sequencing machine

## Slide 5: Outline
Background (optimal vs. heuristic sequence alignment)
Hardware-friendly heuristic alignment for DNA sequences [1]
Adapting hardware-friendly heuristic alignment to protein sequences
  Challenges around protein characteristics
  Algorithmic alignment improvements
  Quality of results & discussion
Future work
[1] Darwin: A Genomics Co-processor Provides Up to 15,000x Acceleration on Long Read Assembly [Turakhia, Bejerano, Dally], ASPLOS’18

## Slide 6: Optimal alignment
Given 2 sequences
  (query sequence)
  (reference sequence)
Insert gaps in sequences such that
  and they “align”
  Subject to some scoring mechanism
Expensive in time & space
  Compute matrix
  Store traceback pointers
  Perform traceback
 | A | C | G | T
A | 2 | -1 | -1 | -1
C | -1 | 2 | -1 | -1
G | -1 | -1 | 2 | -1
T | -1 | -1 | -1 | 2
Cell dependencies:
A | 2 | -1 | -1 | -1
C | -1 | 2 | -1 | -1
G | -1 | -1 | 2 | -1
T | -1 | -1 | -1 | 2
 | A | C | G | T
Notes: For simplicity I’m illustrating alignment with DNA
Each cell remembers the neighbor it used to compute its value

## Slide 7: Heuristic alignment
Left extension
Prune search space
  Take seeds of fixed size from
  Find seed hits in
  Extend hits to the left (and to the right)
  Perform traceback
Good acceleration requires
  Traceback done in hardware
  Keep all traceback state in on-chip memory
  Restricts size of the extension
   Cannot find long extensions
Notes: Use seed hit location as an anchor to know where to end the alignment

## Slide 8: Outline
Background (optimal vs. heuristic sequence alignment)
Hardware-friendly heuristic alignment for DNA sequences [1]
Adapting hardware-friendly heuristic alignment to protein sequences
  Challenges around protein characteristics
  Algorithmic alignment improvements
  Quality of results & discussion
Future work
[1] Darwin: A Genomics Co-processor Provides Up to 15,000x Acceleration on Long Read Assembly [Turakhia, Bejerano, Dally], ASPLOS’18

## Slide 9: Heuristic hardware-friendly alignment GACT algorithm [1]
Overlapping tile-based alignment
  Tile size,
  Overlap amount,
Algorithm
  Compute single tile
  Traceback to within cells of tile border
  Place next tile at traceback endpoint
Constant on-chip traceback state memory
 Traceback can be done in hardware
[1] Darwin: A Genomics Co-processor Provides Up to 15,000x Acceleration on Long Read Assembly [Turakhia, Bejerano, Dally], ASPLOS’18

## Slide 10: GACT performance
Developed for DNA long read assembly
Heuristic
  But finds optimal extensions for
Open questions
  Can GACT be adapted to obtain optimal protein extensions?
  Are values of applicable to other datasets?

## Slide 11: Outline
Background (optimal vs. heuristic sequence alignment)
Hardware-friendly heuristic alignment for DNA sequences [1]
Adapting hardware-friendly heuristic alignment to protein sequences
  Challenges around protein characteristics
  Algorithmic alignment improvements
  Quality of results & discussion
Future work
[1] Darwin: A Genomics Co-processor Provides Up to 15,000x Acceleration on Long Read Assembly [Turakhia, Bejerano, Dally], ASPLOS’18

## Slide 12: Design space exploration
DNA
  Better alignments by increasing
  only / only / both
Proteins
  250K alignments
  Never reach 100% optimal alignments
  QoR decreases with high overlap
Notes: Only showing a subset of the results here for legibility and so we can see the data trends

## Slide 13: Classifying GACT behavior
Obtains optimal alignment
Premature traceback termination
  Sensitivity to GACT’s placement of current tile
Traceback divergence
  Traceback in previous tile drives placement of current tile
  Erroneous traceback in previous tile  current tile will be misplaced
Notes: 1) Traceback always matches the optimal traceback, but just termintes too early

## Slide 14: Premature traceback termination
Proteins are sensitive to tile placement
More tile overlap better alignment
Occasionally results in worse alignments

## Slide 15: DNA vs. protein substitution matrices
DNA
  Homogeneous matrix
    E.g. +2 for matches
    E.g. -1 for mismatches
Proteins
  Heterogeneous matrix
    All matches weigh
    Some mismatches weigh
  High magnitude variations
    Some amino-acid pairs weigh others
A | 2 | -1 | -1 | -1
C | -1 | 2 | -1 | -1
G | -1 | -1 | 2 | -1
T | -1 | -1 | -1 | 2
 | A | C | G | T

## Slide 16: GACT hardware resource requirements
DNA
Homogeneous substitution matrix
PE hardware resources
  1 comparator, 2 registers, 1 multiplexor
Large number of PEs can fit on a device
Increased GACT alignment throughput
Proteins
Heterogeneous substitution matrix
PE hardware resources
  1 on-chip memory to store matrix
Limits number of PEs that can fit on a device
Decreased GACT alignment throughput
GACT can be efficiently implemented as a systolic array of Processing Elements (PE)
Each PE handles 1 cell in scoring matrix
Notes: There is not just 1 substitution matrix, so we can’t hard-code the matrix in our hardware design

## Slide 17: Traceback divergence
Minor traceback error in previous tile
   Large traceback error in current tile
Can solve issue by
  Increasing
  But we want to avoid increasing on-chip memory constraints
What we would like
  Algorithm that can achieve better alignments with small
  Quadratically less resources
Tile misplaced

## Slide 18: Improving the heuristic – Multi-pass GACT
Idea
  Traceback drives placement of tiles
  Increase confidence in previous tile’s traceback
  Reduce probability of divergence in current tile
Multiple passes over 2 consecutive tiles
  Compute tile 1
  Traceback until border
  Compute tentative tile 2
  Recompute tile 1 (using elevated overlap region)
  Final traceback of tile 1

## Slide 19: Quality of results & discussion
Dataset
  11 bacterial genomes ( 25K proteins)
  A few outliers with length > 30K
  250K protein alignments
Results
  Alignment scores improve between 0% and 29’000%
  On average 14% better (few alignments are very long)
Many cases where multi-pass GACT does not work well
  Large vertical/horizontal stretches in the traceback
  Tiles placed diagonally  cannot “cross” a large vertical/horizontal stretch

## Slide 20: Outline
Background (optimal vs. heuristic sequence alignment)
Hardware-friendly heuristic alignment for DNA sequences [1]
Adapting hardware-friendly heuristic alignment to protein sequences
  Challenges around protein characteristics
  Algorithmic alignment improvements
  Quality of results & discussion
Future work
[1] Darwin: A Genomics Co-processor Provides Up to 15,000x Acceleration on Long Read Assembly [Turakhia, Bejerano, Dally], ASPLOS’18

## Slide 21: Seeding a protein-based heuristic aligner
Observations
  Large protein alphabet size
  Long seed hits improbable
  Multi-pass GACT works well on relatively “diagonal” tracebacks
Idea
  Use piecewise alignment algorithm
  Seeding algorithm can help with this
    Tile alignment matrix
    Compute small local alignments in parallel
    Find stretches of high-scoring tiles
    Merge stretches

## Slide 22: Conclusion
Protein alignment is compute-intensive  hardware-acceleration
  Long alignments (lengths span 4 orders of magnitude)
  High on-chip memory resource requirements (large alphabet)
  Skewed substitution matrices  existing heuristic aligners miss alignments
Proposed algorithmic improvements for a hardware-friendly aligner
  Trades linearly more work for quadratically less resources
  Increases protein sequence alignment scores
    Avg. 14%
    Max. 29000% (long proteins)